## Slide 1
Finite Element Simulation For Mechanical Design
Dynamic analyses
Prof. Andrea Bernasconi

## Slide 2: 1 D.O.F.
In a system having n d.o.f.
R(t) -> {R}, nodal forces
u -> {D}, nodal displacements
k, c, m scalars -> [K], [C], [M] matrices (in absence of non-linearities, contain only scalars)

## Slide 3: Dynamic analyses
In general, given {R(t)}, one wants to know {D(t)} and its derivatives
This implies an integration over time.
It is possible to have less-demanding objectives:
Frequencies and vibration modes
Frequency response

## Slide 4: Undamped free vibrations

## Slide 5: Damped vibrations
With damping, and if c < cc = 2mw, motion is oscillatory, but the amplitude decreases

## Slide 6: Frequency response
Objective: to find the amplitude of vibrations as an effect of loads that vary sinusoidally with time
Note: if multiple loads are applied, they must have the same frequency

## Slide 7: Frequency response: 1 d.o.f.
After an initial transient period, that vanishes due to damping, the vibration stabilizes
Amplitude is proportional to F0
Phase shift between u and r
Static deformation F0 / k is amplified if W approaches w (resonance)

## Slide 8: Frequency response: 1 d.o.f.
Systems having n d.o.f. have as many natural frequencies as the number of d.o.f.
Resonance is possible when one of more forces have frequencies close to one of the natural frequencies

## Slide 9: Finite Element systems
Terms appearing in the equation are:
[K] stiffness matrix
[M] mass matrix: mij are loads to be applied to the i-th degree of freedom to cause a unit acceleration of the j-th d.o.f.
[C] damping matrix

## Slide 10: Mass matrix
In a FE model, masses (distributed) can be:
lumped
distributed
Example: beam element
M becomes a diagonal matrix
In [K], the j-th column represents the vector of nodal loads that mantain the displacement field created by a unit value of the j-th d.o.f.
Similarly, in [M], the j-th column represents the vector of nodal loads that mantain the acceleration field created by a unit value of the second derivative of j-th d.o.f.
Mass lumping
The displacement field is treated as discontinous

## Slide 11: Distributed masses
Inertia is treated like a distributed load
hypothesis: linear variation of v(x)
The load acting on the element dx
By imposing equilibrium
The M matrix is now full. However, it does not contain mij associated to the rotational degrees of freedom

## Slide 12: Consistent [M]
In a beam element, one has to account also for nodal rotations and the corresponding inertial loads: the direct methods is inadequate
Following the same approach as for [K], applying the virtual work to inertia forces one obtains
[M] is defined as consistent because the same shape functions of [K] are used.
Thus, for a beam element
Which operates on

## Slide 13: Consistent [M]
All previously shown matrices correctly represent the resistance to translational accelerations.
Whether the matrix [M] is consistent or not, proper convergence is assured with mesh refinement if it provides the correct inertia forces for all possible translational accelerations
Particularly, for
compatible elements
fully integrated
[M] consistent
computed wi are upper bounds of the true w (convergence from above)
Note: the model is stiffer -> computed wi are raised

## Slide 14: FEM: undamped free vibrations
Undumped
either constant or zero
Eigenvalue problem

## Slide 15: FEM: eigenfrequencies and vibration modes
Trivial solution, we are not interested in
Eigenvalues -> Eigenfrequencies
The corresponding eigenvectors are the vibration modes
Note: the structure can be modelled as free (no boundary conditions); rigid motions, corresponding to w=0, pose numerical issues, that can be overcome by setting an “eigenvalue shift”

## Slide 16: FEM: eigenfrequencies and vibration modes
Elastic reactions are in equilibrium with inertia loads
Are “modes”: amplitudes are defined up to a multiplicative constant, thus modes are usually normalized
n d.o.f. => n wi, but it is not necessary to evaluate them all, unless in special cases, like impacts, the response of a structure is governed by the first modes only.
Modes are orthogonal wrt [K] and [M]

## Slide 17: Exercise
Find limit w , such that stress in the wire is equal to sall
m = 7.26 kg
w
Steel wire
L = 1000 mm
A = mm2
sall = 235 MPa

## Slide 18: Solve the problem and report your results

## Slide 19: Exercise
Find limit w , such that stress in the wire is equal to sall
m = 7.26 kg
w
Steel wire
L = 1000 mm
A = mm2
sall = 235 MPa

## Slide 20: Problem’s data from Hummer Throw

## Slide 21: Units!!!
Newton’s law
F = m a
m N s:
  Unity acceleration: 1 m/s2
  Unit force: 1 N = 1 kg x 1 m/s2
  masses must be expressed in kg
  density must be expressed in kg/m3
mm N s:
  Unity acceleration: 1 mm/s2
  Unit force: 1 N = 1000 kg x 1 mm/s2
  Masses must be expressed in t = 1000 kg
  density must be expressed in t/mm3

## Slide 22: Number of elements
The most appropriate number of elements depends on the number of modes of interest.
The first modes have a small number of nodes and therefore are properly described by a smaller number of elements than higher order modes.
Example: with only one element it is possible to model the first eigen mode, not the second
Let’s see more in Abaqus
K1 =1.875
K2 =4.694

## Slide 23: Damping matrix
[C] represents a viscous damping term
Common sources of damping in structures are not viscous (e.g. friction in joints)
The contribution of [C] is small, therefore it can be idealized as viscous
Typical values of the damping ratio are x = 0.02 – 0.07

## Slide 24: Proportional damping (Rayleigh)
Arbitrary definition, no physical meaning
Damping depends on frequency. E.g. for a 1 d.o.f. system:

## Slide 25: Proportional damping (Rayleigh)
4 values x1, x2, w1,w2 are chosen and the system solved

## Slide 26: Proportional damping (Rayleigh)
With this definition, one must accept the curve between points 1 and 2 as a satisfactory representation of damping over the range w1<w<w2
It demands infinite damping for w -> 0
Another way is modal damping -> modal equations

## Slide 27: Modal equations
I step)
Normalization of the eigenvectors with respect to the mass matrix
And therefore
Coordinate transformation: from PHYSICAL to MODAL, in the solution of the problem

## Slide 28: Modal equations
II step)
Build the modal matrix [F]
n is the number of the free d.o.f. (not suppressed by constraints or boundary conditions)
And the matrix
For the orthogonality of modes

## Slide 29: Modal equations
III) step
{D(t)} is expressed as a combination of the n {D}i, i.e.
zi are the modal coordinates

## Slide 30: Modal equations
IV step)
substitute {D} and its derivatives with and its derivatives, and pre-multiply by [F]T
hence

## Slide 31: Modal equations
V step)
Express damping as:
proportional
in this case [CF] is diagonal
b) modal
In any case the equations are fully uncoupled
Function of time

## Slide 32: Modal equations: analysis
These equations can be integrated:
in closed form, only in few cases
more in general, by direct integration, for known boundary conditions
Boundary conditions are expressed as known values of {D} and {dD/dt} at t=0

## Slide 33: Modal equations: boundary conditions
To obtain the values of {z} and {dz/dt} at t=0

## Slide 34: Modal equations: advantages
For many practical problems, we need not use all n modes, only the lowest few m modes need be retained, with m << n
Therefore, only the first m modes need to be evaluated.
Suitable for problems where only the first modes are activated.
Not suitable for shock loadings, where higher order modes can be activated.

## Slide 35: Frequency response: 1 d.o.f.
Need being considered all modes up to the first frequency greater than 2W

## Slide 36: Exercise

## Slide 37: Frequency response: example

## Slide 40: FRF plot at node 18

## Slide 41: Assignments
Estimate f1
Compare static U1 with dynamic U1 of node 18 (i.e. node 16 in the textbook - different modellers may assign different node numbers) at 122 Hz
Estimate U1 of node 18 at 122 Hz
Compare static RF with dynamic RF at 122 Hz at node 1

## Slide 42: Estimate f1
m2
m1
m2/2
m2/2
m1/2
m1/2

## Slide 43: Estimate f1
m1
m1
m1/2
m1/2
m2/2
m2/2
keq

## Slide 44: Estimate f1
F = 1
d = 1 / keq
length = 2 a
length = 3 a

## Slide 45: Compare static U1 with dynamic U1 of node 18 at f4

## Slide 46: Compare static RF with dynamic RF at f4 at node 1

## Slide 47: Estimate U1 of node 18 at f4
p4 = 0.684531 x 3000 = 2053.6
f4 = 123.54
w4 = 2p (123.54) = 776.2
z4 = (p4/w42)/(2 x) = (2053.6 / 776.22)/(2 x 0.02) = 0.0852
U1 (node 18) = z4 x 0.880017 = 0.075 mm

## Slide 48: Time domain analyses
Direct integration, step by step
There are n time steps, separated by a given Dt
At each step
Dt, 2 Dt, 3 Dt, …, n Dt
The equation of motion is
if the problem is linear, otherwise
By direct integration, conditions at step n+1 are calculated from
the equation of motion
a difference expression
known conditions at one or more preceding step times

## Slide 49: Time domain analyses
The discretization of the time derivatives is usually achieved by the finite differences' method.
According to the formulation of the finite differences (forward, backward, central), two classes of methods exist:
Implicit, which uses a difference expression of the type
combined with the equation of motion at step n+1
Explicit, which uses a difference expression of this type
combined with the equation of motion at step n

## Slide 50: Implicit and explicit methods
Explicit methods are conditionally stable
there exist a critical Dt, above which the solution becomes unstable
the solution at each step is faster (the matrix of the coefficients of {D}n+1 can be made diagonal)
The critical Dt is usually small; therefore, many more time steps are required than by implicit methods, but the solution of each step is fasted (up to 4000 times for 3D problems)
suitable for wave propagation problems (impact, burst, crash)
Implicit methods are unconditionally stable
Solation is stable for any Dt (although accuracy will suffer …)
The coefficient matrix of {D}n+1 cannot be made diagonal -> higher computational costs at each step (but fewer steps that with an explicit solver)
Suitable for structural problems (when the rise time and duration of the load exceeds a few multiples of the time required for a sound wave to travel through the structure)

## Slide 51: Explicit methods
Centra differences
Retaining only the terms up to Dt2

## Slide 52
Substituting
in
one obtains

## Slide 53: Stability
Equation
is conditionally stable, i.e. it can be shown that the solution may diverge unless
where frequency wmax and its period Tm corresponds to the highest natural frequency of